## Slide 1: High Power Efficiency Design Approach of a LLC Resonant Converter for UPS Battery Charger Application and Battery Charge-Discharge Regression Model
Graduatıon project
Turhan Can KArgın

## Slide 2
SUPERVISOR: Assoc. Prof. Savaş ŞAHİN
CO-SUPERVISOR: Fırat DEVECİ – TESCOM Elektronik A.Ş.
This work is supported by the Scientific and Technical Research Council of Turkey (TUBITAK) under 2209B-Bachelor Final Thesis Focused on Industry Program with Project number 1139B411900874.
This work is presented in 2nd International Conference of Applied Sciences, Engineering and Mathematics (ICASEM 2020).
High Power Efficiency Design Approach of a LLC Resonant Converter for UPS Battery Charger Application and Battery Charge-Discharge Regression Model

## Slide 3: Introduction
This presentation present the analysis and design considerations for a half-bridge LLC resonant DC-DC converter. Using the fundamental approximation, the voltage and current waveforms are analyzed and the gain equations are obtained. Half-bridge LLC resonant converter has 400V input and 48V/3.1A output.The circuit is simulated using PSIM software. In addition, it is presented as secondary output to find the charge-discharge models under varying conditions by deriving the regression models with machine learning algorithms where the battery electricity energy consumption, battery status and temperature data can be analyzed.

## Slide 4: LLC Rezonant Converter
1. The advantages of LLC Rezonant Converter
2. Why to use as UPS Battery Charger
Block diagram of a universal battery charger

## Slide 5: Circuit Design
  Define the system specifications and determine the maximum and minimum voltage gains of the resonant network
A schematic of half-bridge LLC resonant converter

## Slide 6: Circuit Design
  Calculate the Equivalent Load Resistance and Design the resonant network
Peak Gain (Attainable Maximum Gain) vs. Q for Different m Values
With m value chosen in previous slide, read proper Q value from the peak gain curves in Figure that allows enough peak gain. Considering the load transient and stable zero-voltages-witching (ZVS) operation, 10~20% margin should be introduced on the maximum gain when determining the peak gain.

## Slide 7: Circuit Design
  Design the transformer and select the resonant capacitor
Typical Gain Curves of LLC Resonant Converter
From the gain curve of Figure, the minimum switching frequency will be obtained

## Slide 8
Therotical calculation results
Design Specification
Define Ratio ‘n’
Select Value of k and Q
Define Value of Mmax-Mmin
Check M, k and Q Graph
Are the values of M, k and Q is in the Limit.(ZVS)
Calculate ‘Cr’
Calculate ‘Rac’
YES
NO
Design results are calculated as;
= %96= 363.276V k = 9.4
= 150 W = 400 V
= 148.8W = 1.1066
= 1.22
= 251.9 Ω = 19.03 nF
= 110 uH = 600 uH
= 57.78 uH = 2.879 uF
= 542.2177 uH= 36
= 8 = 1.044 A
= 495 V Q = 0.302
Circuit design results

## Slide 9: Simulation Results

## Slide 10: Simulation Results
Output Voltage (V) and output current (A) of the LLC Resonant Converter

## Slide 11
= %9
MOSFET voltage (V) and current (A) achieving soft switching

## Slide 12
Typical Voltage (V) and current (A) waveforms of half-bridge LLC resonant converter
Simulation Voltage (V) and current (A) waveforms of resonant converter

## Slide 13: PCB Design

## Slide 14: Regression Models with Machine Learning
Results Regression Models | Root Mean Square Error | Score
SVR | 1057.0299 | 0.0008
Linear Regression | 77.2032 | 0.9946
LGBM Regressor | 465.0893 | 0.8065
XGB Regressor | 93.0894 | 0.9922
Gradient Boosting Regressor | 70.8098 | 0.9955
Random Forest Regressor | 67.843 | 0.9959
Decision Tree Regressor | 128.161 | 0.9853
MLP Regressor | 994.0306 | 0.1164
K-Neighbours Regressor Polynomial Regressor | 104.8204 70.5056 | 0.9901 0.9956
Results Regression Models | Root Mean Square Error | 
SVR | 1057.0299 | 0.0008
Linear Regression | 77.2032 | 0.9946
LGBM Regressor | 465.0893 | 0.8065
XGB Regressor | 93.0894 | 0.9922
Gradient Boosting Regressor | 70.8098 | 0.9955
Random Forest Regressor | 67.843 | 0.9959
Decision Tree Regressor | 128.161 | 0.9853
MLP Regressor | 994.0306 | 0.1164
K-Neighbours Regressor Polynomial Regressor | 104.8204 70.5056 | 0.9901 0.9956
Regression model comparison using Python

## Slide 15: Regression Models with Machine Learning
Visualization of battery discharge regression models

## Slide 16: Thank You